Expedited Process Completion Documentation

Please carefully review your Conditional Approval email (and any attachments) for any additional documentation requirements that are specific to your application. After reviewing the Conditional Approval email, please use this checklist to ensure that you provide all necessary project completion documentation.

For any documents provided by National Grid, please verify that the legal contact information has been entered correctly. If corrections or updates need to be made, please submit an up-to-date copy of the Legal Information Document. Updated versions of all forms may be found on National Grid’s “Interconnection Documents” webpage: http://www9.nationalgridus.com/narragansett/business/energyeff/4_interconnection-documents.asp.

| For DG Application: RI-XXXXXXXX_Name | Customer Submission | Utility Approval (or Comments) |
| --- | --- | --- |
| The Interconnecting Customer must complete (and return) the following items promptly after they have been provided by National Grid. |
| 1 | Interconnection Service Agreement (ISA) Note: Initials are required on every page at the bottom. | C |  |
| a) | Exhibit G | Interconnection Service Agreement | C |  |
| b) | Exhibit H | Agreement between the Company and the Company’s Retail Customer | C (or N/A) |  |
| Note: In the Expedited Process, the Exhibit H will be provided by National Grid and must be submitted in any instance where the owner and/or operator of the DG system is not the named responsible party on the host retail electric billing account (also known as the “Host Customer” or “Retail Customer”). |
| Once the signed ISA has been submitted, National Grid will send any System Modification invoices to the Interconnecting Customer (as indicated on the most recent Legal Information Document and based on the terms and conditions of the ISA). Invoices should be paid using the instructions on the invoices. |
| 2 | The full System Modifications costs have been paid. Due prior to construction (as per the payment plan in the ISA) | C (or N/A) |  |
| For an Expedited Process application, a Witness Test will be required if redundant relays have been required (as identified in the technical standards and/or review process). If the need for a Witness Test has been identified during the review process (or in the ISA), Interconnecting Customers in the Expedited Process should refer to the “Standard Process Completion Documentation” checklist and the Witness Test Process webpage for more information. Note: A Witness Test may otherwise be required as permitted by the Interconnection Tariff. |

|  | Customer Submission | Utility Approval (or Comments) |
| --- | --- | --- |
| The Interconnecting Customer must complete and submit the following items prior to requesting that a new meter be installed (or scheduling a witness test). |
| 3 | Documentation for Metering (for net metering provide “a” OR for qualifying facilities >60kW provide “b” & “c”) | C |  |
| a) | Schedule B | Additional Information Required for Net Metering Service http://www9.nationalgridus.com/non_html/RI_DG_Schedule_B.docx | C (or N/A) |  |
| b) | Qualifying Facility Forms (Need if >60kW) | Agreement to Purchase under the Rate Tariff (Schedule A). Refer to National Grid’s full Rate Tariff | C (or N/A) |  |
| c) | Form 556 (Need if 1MW or larger) | FERC Qualifying Facilities Certificate https://www.ferc.gov/docs-filing/forms/form-556/form-556.pdf | C (or N/A) |  |
| 4 | Exhibit B2 | Expedited/Standard Certificate of Completion (must be signed by the local or Federal code official at the time of the electrical inspection) | C |  |
| 5 | Commissioning Memo | Must be on Electrical Company/ Installation Contractor letterhead, signed and dated by the Electrical Company/ Installation Contractor AND include/provide all of the following statements with Frequency(Hz) Listing: | C | Do Inverter relays’ settings meet NPCC Frequency requirements? |
| a) | The system passed the “2 seconds shutdown, when utility disconnect is open” test. | C |  |
| b) | The system passed the “5 minutes before restart, after utility disconnect is closed” test. | C |  |
| c) | A visual inspection of the system confirms that the system matches the As-Built electrical One or Three line diagram dated_______. | C |  |
| d) | The relay frequency settings identified in the relevant interconnection standards R.I.P.U.C. No. 2078, Section 4.2.4 Frequency and in the Screening Memo and/or Supplemental Review Memo are adhered to and have been tested. List Inverter internal relay frequency (Hz) and time. Provide field proof, via statement/table in memo, if field difficult, providing additional support documentation and noted as such in Commissioning Memo is acceptable. | C |  |
| 6 | A complete As-Built P.E.-Stamped One-Line Diagram (must be signed and dated on the day of the commissioning test by the installation contractor that performed the commissioning test) | C |  |
| 7 | Evidence of Insurance | Refer to the ISA and the Interconnection Tariff for insurance requirements. The original must be mailed to the address in the ISA. | C OR: |  |
| a) | ≤50kW Net Metering | As per the ISA, evidence of insurance is not required if net metered and ≤50kW | N/A |  |
| b) | Government Entity | As per the ISA, some Facilities owned by Government Entities are exempt from this requirement | N/A |  |

|  | Customer Submission | Utility Approval (or Comments) |
| --- | --- | --- |
| 8 | Utility Revenue Meter Phone Number or Wireless Meter Payment | All accounts with >60kW of generation capacity capable of exporting power to the National Grid Electric Power System (EPS) must install a dedicated phone line at the Utility Revenue Meter. Refer to the National Grid Phone Line Installation Guide for the most up-to-date specifications. If a Wireless meter was requested, the $800 fee shall be paid | Phone #: (000)000-0000 C (or N/A) |  |
| The Interconnecting Customer must provide clear pictures of the following pieces of equipment and plaques in both (a) wide-angle shots to provide context of the equipment locations and (b) close-up shots to ensure the legibility of any signage or permanent plaques. Note: Any permanent plaques must be suitable for the environment in which they are located and rated to last for the lifetime of the generation equipment. No stickers of any type will be accepted as permanent plaques for equipment that is located outside. All plaques as described in NEC 705.10, 705.12 (7), 690.56, 692.4 and 705.70 shall be installed when applicable. |
| 10 | All generator(s) or inverter(s) | C |  |
| 11 | Utility Revenue Meter, including the following (as applicable): | C |  |
| a) | If a phone line is required, the picture must show the phone line. | C (or N/A) |  |
| b) | A permanent plaque (visible at eye level) that includes a warning about the generator installed. | C |  |
| c) | If the AC Utility Disconnect Switch is not grouped with and adjacent to the Utility Revenue Meter, a permanent plaque (visible at eye level) that clearly identifies the location of the AC Utility Disconnect. | C (or N/A) |  |
| 12 | AC Utility Disconnect Switch (located outside, 24/7 accessible) | C |  |
| a) | A permanent plaque (visible at eye level) that reads “AC Utility Disconnect Switch”. | C |  |
| 13 | Current Limiting Device(s) (e.g. show fuses and/or circuit breakers) If tap is not in Main or Sub Panel, show location of tap (before/behind Meter). | C |  |
| 14 | Customer-owned Production Meter(s) (if installed) | C (or N/A) |  |
| a) | If the customer-owned production meter is a revenue-grade meter (or otherwise looks similar to a National Grid utility revenue meter), a permanent plaque (visible at eye level) that reads “Customer-Owned Production Meter”. | C (or N/A) |  |
| 15 | Customer-owned Transformer(s) (if installed) | C (or N/A) |  |
| 16 | Any new and existing Service Equipment (on/in/at the building) | C |  |
| a) | At each piece of Service Equipment (that is not grouped with and adjacent to all other pieces of service equipment on/in/at the building), a permanent plaque (visible at eye level) that describes and/or depicts the locations and accessibility of all pieces of service equipment on/in/at the building. | C (or N/A) |  |
|  |  | Customer Submission | Utility Approval (or Comments) |
| 17 | Point of Common Coupling (PCC) as identified in the ISA (choose all applicable options “a”-“d” below) | C |  |
| a) | If the PCC is at a pole-mounted service transformer, the permanent plaque(s) required for the Utility Revenue Meter is sufficient. | C (or N/A) |  |
| b) | If the PCC is at a pad-mounted service transformer, a permanent plaque (visible at eye level, located on the right door of the pad-mounted service transformer) that includes a warning about the generator installed. | C (or N/A) |  |
| c) | If the PCC is at a secondary or primary meter, the permanent plaque(s) required for the Utility Revenue Meter are sufficient. | C (or N/A) |  |
| d) | If the AC Utility Disconnect Switch is not grouped with and adjacent to the PCC, a permanent plaque (visible at eye level) that clearly identifies the location of the AC Utility Disconnect. | C (or N/A) |  |

Please review the Conditional Approval email (and any attachments) for any additional documentation requirements that are specific to your Interconnection Application!

| After National Grid has completed any EPS modifications (as identified in the ISA) and the Interconnecting Customer has successfully submitted/completed all of the items listed above (and/or identified in the Conditional Approval email) National Grid will complete the following actions. |
| --- |
| 1 | Installation of new ‘net’ and/or ‘bi-directional’ meter (if applicable) | N/A | C (or N/A) |
| a) | Requested | Once all other items have been satisfactorily completed, National Grid’s DG group will request the installation of a new meter. | N/A | C (or N/A) |
| b) | Installed | A new meter installation could take up to three weeks for installation after documentation and phone line are provided. | N/A | C (or N/A) |
| 2 | Authorization to Interconnect | This is an official authorization to activate and operate your generating system. | N/A | C |
| Warning: Operating your generator prior to receiving the Authorization to Interconnect may cause damage to National Grid’s electric power system or other customers’ equipment and will likely cause billing errors, which will result in additional charges on the customer’s bill. |

For additional information about the distributed generation interconnection process, please refer to National Grid’s Interconnection Process webpage for Distributed Generation: http://www.nationalgridus.com/narragansett/home/energyeff/4_interconnection-process.asp.